## Slide 1: MODULE 1: PURCHASING CLEAN VEHICLES
The sole responsibility for the content of this presentation lies with the Clean Fleets project. It does not necessarily reflect the opinion of the European Union. Neither the EACI nor the European Commission are responsible for any use that may be made of the information contained therein.
Notes: <number>

## Slide 2: 1.1: MOTIVATIONS FOR CLEAN VEHICLE PROCUREMENT
Notes: <number>

## Slide 3: AIR QUALITY
    PM10
    NO2
    NOx and NO2
    PM2.5 – the next big
    (very, very small) thing
Notes: An overview of the differences between, and issues associated with, local air pollutants that effect air quality:
An example script could be: “Improving air quality in urban areas is an important driver for clean vehicle procurement. I’m going to give you a “whistle stop tour” of air quality. Why it’s a problem - how it is measured – where it comes from and how it is being solved.
The two main pollutants which we are concerned about the most at the moment are:
PM10 – this is very small particles of dust less than 10 microns (hence the name…)
NO2 – Nitrogen Dioxide is a problem, however depending on the atmospheric conditions (amount of ozone and sun) NO2 or NO (Nitrogen Oxide) or even, in very small quantities of NO3 may be produced. So for measuring purposes people tend to bundle them all up and call it NOx (Say N – O – X, then repeat NOx)
In the coming years PM2.5 will become more of an issue, what do we think PM2.5 means? (Ask the audience)
You are right/wrong – it refers to particles under 2.5 microns, these are the smallest PM10 partials and can go deeper into your lungs.
<number>

## Slide 4: HEALTH IMPACTS OF LOCAL AIR POLLUTANTS
    Premature death
    Asthma
    Respiratory illness
    Various types of cancer
    Cardiovascular illness
Notes: It is estimated that fine particles have an impact on mortality equivalent to 4,267 deaths in London in 2008, within a range of 756 to 7,965.
<number>

## Slide 5: MONITORING POOR AIR QUALITY
Notes: London is one of the best cities in the world at monitoring its air quality.
Due to the fact that it monitors its air quality well, it appears to have terrible air quality...... indeed it does have terrible air quality, but so do most major cities in the world....
<number>

## Slide 6: PM10 ANNUAL MEAN
Notes: This shows the sites in London which stayed below and which breached the EU thresholds on the PM10 annual mean last year i.e. the mean of PM10 monitored over a year. As you can see all but one of the sites in London met this target.
<number>

## Slide 7: PM10 DAILY MEAN
Notes: This is not quite such a good a picture. There is a limit to the mean of PM10 which can be detected in a day, this must not be breached more than 35 times in a year. As you can see 7 sites did not manage this and many more did meet the target, however they were close to not meeting the target.
<number>

## Slide 8: NO2 ANNUAL MEAN
Notes: It is even worse for this one! In the same way as PM10, there is a limit to the annual mean for NO2 which many sites in London do not meet.
<number>

## Slide 9: NO2 HOURLY MEAN
Notes: This is not so bad, but still a long way from compliance. There is a average level of NO2 over an hour which must not be breached more than 18 times in a year.
These images are shown as a demonstration of what almost all cities in the world are facing. The limits on PM10 and NOx are based on World Health Organisation limits and meeting them is a major challenge which the procurement of clean vehicles can help with.
<number>

## Slide 10: SOURCES OF AIR POLLUTION
    Saharan dust
    Industry
    Break and tyre wear
    Construction
    Transport
    Your city, does it exceed local air pollution limits?
Notes: As you can see there are various sources of air pollution in cities.
The reality is that the vast majority of air quality associated issues would disappear if vehicles were banned from cities. This is obviously not possible, so ensuring that only the cleanest vehicles are used can go a long way to help.
Do you know if your city exceeds its limits? It is suggested that when doing this part with your trainees a) research where the participant come from and test them on their city b) change the provisos slides to your capital city.
<number>

## Slide 11: EURO STANDARDS
    Heavy vehicles Euro VI
      All new vehicles
    Light vehicle Euro 6
      All new M1(cars) from September 2014
      N1i vans from September 2014
      N1ii, N1iii, N2 vans from September 2015
Notes: The Euro standards are put in place by the EU to ensure that newly manufactured vehicles are as clean as possible. There have been several incarnations and we are at the sixth stage now. Roman numerals are used for heavy vehicles (e.g. Euro VI) and numbers are used for light vehicles (e.g. Euro 6).
These are only designed to deal with air quality associated emissions, not CO2.
<number>

## Slide 12: GLOBAL AIR POLLUTION
    CO2e
    Transports contribution circa 22%
    EU targets
    National targets
    CO2 - a product of burning fossil fuels
Notes: Local air pollutants are very real and ‘in your face’ (i.e. apparent). This means they often get quite a high standing in local authority priorities. Global air pollution, such as CO2 is also of great importance for all the well established reasons associated with climate change. If you would like to go into this topic further with your trainees, our suggested reference is the most recent Intergovernmental Panel on Climate Change (IPCC) Reports – currently the Fifth Assessment Report: http://www.ipcc.ch/
People often refer to “CO2e” – this means CO2 equivalent emissions, this includes other gases, such as Methane which is far more potent than CO2 but is produced in far lower quantities.
There are various targets, it is suggested you read up on your national targets before presenting this.
<number>

## Slide 13: WHY BURN LESS?
    Contributes to climate change
    Contributes to poor air quality
    Often from unstable regions
    Price subject to global fluctuations
    Globally, the EU wants to show leadership in moving away from fossil fuels
Notes: There are a number of reasons to burn less fossil fuels.
Unfortunately, if it were easy we would not all be here learning about how to integrate low emissions vehicles into fleets!
<number>

## Slide 14: ALTERNATIVE FUEL OPTIONS
Source | Available | Pro | Con | The near future
Natural gas | Limited in most countries | Fuel available from secure regions / can be biogas | Produces (less) CO2 and AQ | Used for heavy vehicles and light vehicles in some countries
Biofuels | Limited in most countries | Lifecycle emissions low | Concern over food security | Used for heavy vehicles and light vehicles in some countries
Electricity | Limited | Potentially zero emission | Power stations produce CO2 | Used for light vehicles / short duty cycles
. Clean Buses: Experiences with Fuel and Technology Options
Notes: Emphasise that this is a broad EU wide overview on technology options and that things may differ in specific countries. Incorporate more detailed information about the uptake of these fuel/ technology types in your own country where possible.
For further reading - the Clean Fleets Bus Report goes into depth on this issue
This publication draws together information on the environmental performance, cost and practical aspects associated with 17 different fuel and technology types. Experiences have been taken from over 100 public authorities and transport operators across Europe.
<number>

## Slide 15: WHAT CAN WE DO?
    Step 1: Reduce demand
    Step 2: Replace fossil fuels with alternative fuels and technologies
Notes: <number>

## Slide 16: REDUCE DEMAND – SUSTAINABLE URBAN MOBILITY
    The hierarchy of modes
        Walking and cycling
        Public transport
        Shared transport (car sharing etc)
        Private cars
        Helicopter / private jet
Notes: Do you even need to use a vehicle at all? Perhaps ask your trainees how they get to work in the morning, and have they ever experimented with trying public transport, walking or cycling?
<number>

## Slide 17: REDUCE DEMAND – SUSTAINABLE URBAN MOBILITY
    The hierarchy of modes
        Walking and cycling
        Public transport
        Shared transport
        Private cars
        Helicopter / private jet
Notes: Pause for laughs, if no one laughs explain the joke, if they still refuse to laugh storm out of the room.
<number>

## Slide 18: REDUCE DEMAND – SUSTAINABLE URBAN MOBILITY
    The hierarchy of modes
        Walking and cycling
        Public transport
        Shared transport
        Private cars
        Helicopter / private jet
Notes: This kind of hierarchy has other benefits, for example it has been shown that more walking and cycling results in healthier and happier people.
<number>

## Slide 19: REDUCE DEMAND – SUSTAINABLE URBAN MOBILITY
    The hierarchy of modes
        Walking and cycling
        Public transport
        Shared transport
        Private cars
        Helicopter / private jet
Notes: Also, the impact on congestion can be fairly prominent.
There are various ways to encourage people out of their cars, these can include
Harder measures like congestion charging
Softer measures like “Car Light” in London which tries to identify people who under use their cars and suggest they move to car clubs / cycle etc.
<number>

## Slide 20: REDUCE THE IMPACT OF FREIGHT – SUSTAINABLE URBAN MOBILITY
    Freight transport
        Freight logistic centres
        Timing of deliveries
        Re-routing of freight
      There are many examples of good practices
        Numerous urban freight logistics schemes from CIVITAS
        Stockholm Royal Docks (Construction consolidation hub)
Notes: You as a procurer have the ability to demand this kind of stuff from your suppliers.
Examples:
CIVITAS: http://www.civitas.eu/thematic-categories/urban-freight-logistics
Stockholm: http://www.ndslogistik.se/kommunikation/film
Also, if you do decide to have freight – particularly construction freight it is possible to lessen the impact by using CADS – dust suppressant.
<number>

## Slide 21: PROCURERS ROLE– SUSTAINABLE URBAN MOBILITY
    Procurers have an important role to play in this
    Challenge preconceptions
        Why do you need a private car?
        Why do you need to use a car at all?
        Why are you delivering everything individually?
        Why can’t we invest in an electric bus line?
Notes: Suggest to your trainees that, as procurers, they should be influencing the aspects that we have seen so far. It is part of their job.
Forget the CO2 and AQ issues, think about the money you will save by reducing the size of the company’s vehicle fleet.
Having said that, the old adage stands: ‘Nobody ever got fired for buying a Ford Transit’ This means it is very important to get higher level support from the key stakeholders, i.e. bosses. This will be covered in more detail later today.
<number>

## Slide 22: 1.2: ALTERNATIVE FUELED CARS AND VANS
Notes: <number>

## Slide 23: ALTERNATIVE FUELED CARS AND VANS
    EU legislation
    Cars: 2015 fleet average = 130g CO2/km
      2021 fleet average = 95g CO2/km
    Vans: 2017 fleet Average = 175 g CO2/km
      2020 fleet average = 147g CO2/km
    Meeting these target is only achievable with significant market penetration of electric vehicles
Notes: All figures are fleet averages – i.e. An average of all the vehicle models offered by a manufacturer. Not all individual vehicles must meet the target.
DO NOT use these as a target! As the figures are an average of all vehicles they include supercars, SUVs etc. You can aim for less than 100 gCO2/km for most small and medium cars, and you can get a relatively well powered Transit connect style van for less than 140 gCO2/km
Also to bear in mind: When calculating the fleet averages, an EV = 2 cars in 2020=, an EV = 1.66 cars in 2021 and an EV = 1.33 cars in 2022.
Therefore vehicle manufacturers will be trying to peddle zero emission vehicles to you, as they have to sell them to meet their emissions targets.
<number>

## Slide 24: WHAT IS AVAILABLE
Technology | Car | Vans
Petrol | ✓ | ✓
Diesel | ✓ | ✓
Hybrid | ✓ | After market conversion
Plug in hybrid | Medium (C, D and SUV segment) | X
Range Extended electric | Small and medium (B and C segment) | X
Electric | ✓ | OEM small vans and Aftermarket conversions
Gas | In some countries | In some countries
Biofuel | In some countries | In some countries
Hydrogen | X | X
Notes: Point out
Plug in and range extended vehicles are constantly becoming more available in different car models. As are electric vehicles. It feels like there is a new model every week!
Gas is available in Italy, becoming more prevalent in Germany and Switzerland. All countries will have to have a gas refuelling network in place by 2020 – this is an EU law.
Any other factors relevant to the market maturity of each of these fuel/ technology types in your own country.
OEM = Original equipment manufacturer. In this context it means car companies, i.e. not people who buy a car and replace the power train with an electric power train.
<number>

## Slide 25: GENERAL RULES FOR PETROL AND DIESEL (ICE)
      Diesel vehicles are cheaper than petrol over their lifetime
      Petrol vehicles produce more CO2 per Km than diesel vehicles
        Ford Focus – Diesel 88 g CO2/Km vs petrol 109 g CO2/Km
      Petrol vehicles produce less air quality associated emissions
        Ford Focus – Diesel NOx 146 mg/Km vs petrol 32.8 mg/Km
      Petrol vehicles are more suited to urban, stop start driving and diesel vehicles are more suited to out of town driving, at constant speeds.
Notes: Take time to go through these general rules for each of the upcoming technology types – they will be especially relevant later as part of the interactive exercise, where „Fleet manager“ trainees have to decide which type of fuel/ technology options may be most appropriate according to driving patterns and other factors.
ICE = Internal Combustion Engine.
<number>

## Slide 26: GENERAL RULES FOR HYBRID VEHICLES
      Little difference between this and an ICE vehicle
      A stop gap between conventional fuelled and electric vehicles
      They produce slightly less CO2 emissions than conventional petrol car
        Toyota Prius = 89g CO2/Km vs Ford Focus = 109g CO2/Km
      A smaller car could be more appropriate
        Toyota Prius = 89g CO2/Km vs Fiat 500 = 90g CO2/Km
      A diesel car could be more appropriate for non-urban driving
        Ford Focus diesel = 88g CO2/Km
Notes: See previous slide for notes/ relevance
<number>

## Slide 27: GENERAL RULES FOR ELECTRIC VEHICLES
      Vehicles run exclusively on electricity
      Advertised range of up to 160km, assume 60% of this
      Vehicles can be more expensive to purchase, but cheaper over the lifetime due reduced running costs
      Batteries are often leased rather than purchased – price is then similar to an ICE
      The operators have to be trained to plug the vehicle in after every journey
      Can be very suitable for use as a pool car, with a management system in place
      Most charging is likely to happen at ‘home’, many vehicles charging at the same time can require significant grid upgrades = costs.
      At present few countries have a recharging network which can be relied upon. At present only Estonia does.
Notes: See previous slide for notes/ relevance
Point 2:
If you use the heaters, lights, or constantly accelerate hard a driver will use more of the energy in the battery. Therefore when procuring vehicles you need to assume a range 60% of the total advertised range.
<number>

## Slide 28: GENERAL RULES FOR PLUG IN HYBRID AND RANGE EXTENDED VEHICLES
      Vehicles have an engine and a rechargeable battery.
      It is possible to use the vehicle almost exclusively as an electric vehicle, the engine can cut in if the battery runs out.
      The all electric range for a plug in hybrid is approximately 15km
      The all electric range for a range extended electric vehicle is 40-160km
      The vehicles are more expensive than a conventional ICE, but savings can be cheaper over their lifetime
      The operators need to be trained to plug the vehicle in as often as possible to ensure it runs on electricity as often as possible
      If the vehicle cannot be plugged in often, an ICEvehicle should be purchased instead
      If the engine will not be used an electric vehicle should be purchased instead
Notes: See previous slide for notes/ relevance
<number>

## Slide 29: GENERAL RULES FOR GAS AND BIOFUELED VEHICLES
      These vehicles are similar to a conventional ICE vehicle but use alternative combustible material
      Biofuels come from various renewable sources, including crops and waste.
      Gas is the same as domestic gas, which is compressed (CNG). Gas can also come from renewable sources (biogas/biomethane)
      Dedicated refuelling infrastructure is required. At present there is a limited number of countries with this.
Notes: See previous slide for notes/ relevance
<number>

## Slide 30: GENERAL RULES FOR ALTERNATIVE FUELS VEHICLES
      Subsidies exist for some of these technologies
      Look at both leasing and purchasing.
      You may need to challenge existing funding mechanisms
      You may need to challenge current vehicle operation systems to allow for the different fuelling or charging regimes
      Alternative fuelled vehicles sometimes need to be driven a lot to be cost effective
Notes: Look at both leasing and purchasing. Even if you only intend on doing one as with new vehicles costs can be significantly different between the two.
<number>

## Slide 31: ACTIVITY 1
    You got the job! - Fleet manager for ‘Fantasia’
    According to the Mayor’s manifesto, emissions have to be reduced dramatically
    The first thing you do is change your job title, you are now the ‘Mobility manager’
    The second thing you do is plan the procurement of the fleet for the next year
Notes: Trainees may have to refer back to the general rules for alternative technology and fuel types to complete this task.
Use the sheets provided, which have the instructions on how to roll out this training – there are separate sheets for trainers and trainees. The former suggests the kind of questions to prompt people with if they are struggling.
See the next slide for instructions.
<number>

## Slide 32: ACTIVITY 1
    Can you deliver?
      What questions will you have to ask people in the department?
      Provide a menu of 2-3 vehicles for each department?
      Who may you have to challenge?
      What problems will you have to overcome?
Notes: Leave this slide up for the session. Spend 20 minutes on this. Then ask each group to take one of the user types and present back what vehicles they would recommend. After each person sums up ask any questions which have been left unanswered by attendees. Try and foster discussion.
<number>

## Slide 33: 1.3: ALTERNATIVE FUELED BUSES AND HEAVY VEHICLES
Notes: <number>

## Slide 34: ALTERNATIVE FUELED BUSES AND HEAVY VEHICLES
      Euro standards are type approved for an engine rather than a vehicle.
Technology | Bus | Truck
Gas | ✓ | ✓
Biofuel | ✓ | ✓
Hybrid | ✓ | ✓
Plug in hybrid | Trials | Trials
Electric | ✓ | ✓
Hydrogen | Trials | Trials
Notes: This means that buses are not always correctly assessed for emissions as the tests for large engines are designed with a truck’s drive cycle in mind. There is a new drive cycle for buses called SORT, which you should use when making assessments, it has three levels, for Urban, Semi-urban and Rural buses.
<number>

## Slide 35: GENERAL RULES FOR HYBRID HDVS
      The operator will notice little difference between this and a diesel vehicle.
      They are only suited to stop start conditions, such as urban bus routes and refuse collection
      There are emissions savings of more than 30% for the latest hybrid buses compared to diesel buses
      These can fit seamlessly into an existing diesel fleet
      They play a prominent role in many fleets across Europe, such as the Barcelona and London bus fleets
      They are less common in trucks, some refuse collection vehicles availble
      At present they are more expensive to run than conventional vehicles. Approximately 50% higher capital costs with a payback period in excess of 15 years.
Notes: Ensure that all in the room understand that we are referring to buses and trucks. Not vans and cars.
<number>

## Slide 36: GENERAL RULES FOR GAS AND BIOFUELED HDVS
      These vehicles are similar to a conventional ICE vehicle but use alternative combustible material, sometime as a diesel hybrid
      Biofuels come from various renewable sources, including crops and waste.
      Gas is the same as domestic gas and it is either liquefied (LNG) or compressed (CNG). Gas can also come from renewable sources (biogas)
      As many heavy vehicles have dedicated refuelling infrastructure, for example at bus depots, using this technology can work well
      There are various sources for biofuels which need to considered by the procurer
      Gas and biofuel supply is well developed in many parts of Europe, for example Sweden.
      CO2 and air quality associated emission savings vary depending on technology. They are lower and sometimes close to zero.

## Slide 37: GENERAL RULES FOR ELECTRIC HDVS
      You build the charging infrastructure around the bus route
      There are some examples of buses being used operationally, including in China and Nottingham, UK
      There are few examples of electric trucks being used commercially
      There are two charging methods for buses: fast charging and slow charging and three general regimes for charging.
      CO2 is generally reduced (depending on energy production method) PM and NOx are zero from the bus.
      The vehicles are more expensive to purchase, but often cheaper over the lifetime due reduced running costs
Notes:       Point 4:
      a vehicle has a small battery which is fast charged at specific points on the route, such as either end of a bus route
      a vehicle has a large battery which is charged slowly at the depot and lasts the operational cycle of the vehicle
      a combination of the two where a vehicle is charged overnight and ‘topped up’ at a convenient point in the route, include picture of a bus going from fully charged to discharged
<number>

## Slide 38: GENERAL RULES FOR PLUG IN HYBRID HDVS
      The vehicles run like an electric bus, but have an on board diesel engine or generator
      This allows for the use of electric buses but without the range limitations
      Suited to vehicles which run tough duty cycles, such as city centre buses
      This technology is in its infancy in buses, there are some trials taking place, including London and Stockholm
      The electric element of the vehicle can be geofenced. So the vehicle has zero tailpipe emissions when going through areas of poor air quality.

## Slide 39: GENERAL RULES FOR HYDROGEN HDVS
      It is unlikely that you will be involved with an hydrogen vehicle
      They will not be cost effective until at least 2020
      There will be more EU funded large scale trials taking place in the next few years.
Notes: <number>

## Slide 40: ACTIVITY 2
    Tell me about a bus route in your town?
Notes: What does the city do at the moment?
Do you know the current duty cycles?
Do you know what kind of budget do you have?
<number>

## Slide 41: THE BIG PICTURE
    Successful emissions reduction initiatives almost always have roots in policy
    Part of a procurer’s job is to understand the relevant policy documents
    Use these to inform and bolster the procurement of clean vehicles
    Perhaps you can influence these plans
Notes: Explain to your trainees that, as procurers within public institutions it is part of their job to understand the policy context of what they procure.
<number>

## Slide 42: POLICIES AND TARGETS
    Global level targets
    European level policy
    Country level policy
    City/regional level policies
Notes: Ask the audience to name some targets. Ideas at bottom of page if you get stuck:
As procurers, you should be aware of the policies and targets which are relevant to you - it is part of your job to make best use of them.
EV parking privileges (free parking in London)
EV subsidies (20%, up to £5,000 in UK)
Exempt from road tolls (Congestion charge in London)
Covenant of mayors
20/20/20
<number>

## Slide 43: STAKEHOLDER MANAGEMENT
    Identify key people at the earliest stage
    Take them on the journey
      what would the journey look like?
      Where do you start?
      Why are you doing this?
      What is happening now?
      How are the vehicles used?
Notes:       These people will include: have a discussion, who else would they need to include?
      Engineering managers
      Bus Operating companies
      Vehicle users
      senior managers
      Finance director
      Things you may need to do:
      You will need to establish a baseline – understanding what the vehicles are doing now is imperative to understanding how you may change them
      Understand when the vehicles are up for renewal. You may need to start getting people on board more than a year before this. To give time for a trial of new technology.
      You may have to win people over, convince them of the need to do this. Use the targets and policies to develop the argument.
<number>

## Slide 44: HELP, I NEED SOMEBODY
    You are not alone
      Clean Fleets: www.clean-fleets.eu
      Clean Vehicle Portal: www.cleanvehicle.eu
      Civitas - Civinet networks: www.civitas.eu/civinet
      Eltis: www.eltis.org
      Polis: www.polis-online.org
      Covenant of Mayors: www.covenantofmayors.eu
    Others?
Notes:     You are not alone, another authority has probably done what you are doing. Or is planning to do what you are doing. Linkages with other authorities in the same country could work very well.
    Clean Fleets – guidance and advice directly on procurement
    Clean Vehicle Portal – database of all vehicles on EU market, together with information on emissions
    Civitas – Language based regional Civinet networks at officer level
    Iltis – information exchange
    Polis – European network for decision makers
    Covenant of Mayors – commitment to meet 20% reduction in c02 by 2020
<number>

## Slide 45: CASE STUDY: LONDON
    Mayor’s Electric Vehicle Delivery Plan in 2008
      25,000 charging points in London
      100,000 vehicles in the London fleet as soon as possible
      1,000 vehicles in the GLA fleet by 2015
    The impact
      1,300 charge points
      A plan and dedicated budget for ULEVs within TfL
Notes: There are various policies within London which mean that procurement have to take the environment into account – sometimes these need to be looked for and actioned upon.
Although London was unable to make the changes it wanted to, having the policy direction allowed officers within TfL to make some significant changes. Simply put, without the policy direction TfL would not have many electric vehicles. But at the same time without the policy officers taking the policy on TfL would not have a plan or a dedicated budget to procure the vehicles.
<number>