## Slide 1
The sole responsibility for the content of this presentation lies with the Clean Fleets project. It does not necessarily reflect the opinion of the European Union. Neither the EACI nor the European Commission are responsible for any use that may be made of the information contained therein.
MODULE 4: LIFE CYCLE COSTING & PRACTICAL APPLICATIONS OF THE CVD
Notes: <number>

## Slide 2: 4.1: LIFE CYCLE COSTING (LCC): INTRODUCTION AND OVERVIEW
Notes: Try asking a few of your trainees for a definition of life cycle costing before you begin
<number>

## Slide 3: LIFE CYCLE COSTING (LCC)
Also known as.....
    Whole Life Costing (WLC)
        Sometimes means the same as LCC...
        ...but it can also be considered to be broader in scope
        Is most commonly used in the UK...
        …for our purposes it is best avoided
Notes: We feel it is important to go through the following few definitions as they are commonly mixed up.
<number>

## Slide 4: LIFE CYCLE COSTING (LCC)
Also known as.....
    Life Cycle Assessment (LCA)
        NOT the same as LCC!
        = Assessment of lifetime environmental impacts of a product or activity (not necessarily monetised)

## Slide 5: LIFE CYCLE COSTING (LCC)
Also known as.....
    Operational Lifetime Costs (OLC)
        NOT the same – but can be part of overall LCC
        = Monetised environmental costs
        We will look at this next....

## Slide 6: LIFE CYCLE COSTING (LCC)
Also known as.....
    Total Cost of Ownership (TCO)
        The same as LCC for our purposes
        = The total costs associated with buying or leasing a product, from beginning to end.
Notes: One point of debate with your trainees could be whether or not the procurement process itself should be taken into account. Generally it is with life cycle costing (LCC), but is not with total cost of ownership (TCO). This could have bigger implications for trials, demonstrations and more complex procurement procedures that require investments in terms of human resources and money.
<number>

## Slide 7: LIFE CYCLE COSTING
What does LCC/TCO cover?
        Acquisition costs (purchase price & delivery)
        Installation (product/ associated infrastructure)
        Operating costs (including fuel/ energy use)
        Maintenance and repair costs
        Taxes and fees (especially important when comparing alternative fuel/ technology types)
        Disposal costs/ resale value
Notes: <number>

## Slide 8: LIFE CYCLE COSTING
Discussion
  Any further (vehicle related) LCC aspects?
        Let’s look back
  Although the concept of using LCC is fairly obvious, there are often occasions when it is not used by procurers to calculate costs... Why?
  How would we encourage procurers to take LCC into account?
Notes: Barriers to using LCC could be: lack of communication between departments, which makes calculating LCC complex to start with, short term budgets, changing politics within municipalities, intense public scrutiny (and bad feeling) about local government spending cuts on other public services.
Encouraging procurers to use LCC more routinely: Demonstrate savings over the long term to gain buy in from the senior level and passengers. Use the fact that it is a more effective forecasting tool for finance departments.
<number>

## Slide 9: 4.2: OPERATIONAL LIFETIME COSTS (OLC)
Notes: We are going into this option in quite a lot of detail as it is the CVD option that tends to cause the most confusion
<number>

## Slide 10: OPERATIONAL LIFETIME COSTS
The third methodology of the CVD
    It monetises energy consumption, CO2 and pollutant emissions (PM, NMHC, NOx)
    Key point – its just ONE option, you don’t have to use it!
    It is prescriptive – you must calculate it exactly as laid out by the CVD
    To be used correctly it should not be converted into points/ used as part of a weighting that is separate from the financial costs - It calculates a monetary value which should be added to the financial costs of the purchase.
Notes: This is the same slide used in module two to explain the operational lifetime costing method option under the CVD (the harmonised method), but it is good to reiterate it here as it is one of the more complex aspects of the CVD that trainees should be familiar with by the end of the training session.
The Clean Fleets project have been presented with 4 supposed uses of the LCC methodology being used, but only one was correctly carried out. The others used the cost values for emissions stipulated under methodology 3, but were subsequently used as part of other formulas or weightings, rather than simply being added to the LCC costs and presented as a total monetary value
<number>

## Slide 11: OLC – FUEL CONSUMPTION
.
Vehicle type | Fuel consumption (l/100km) | Fuel consumption (l/km) | Fuel conversion factor (MJ/l) | Fuel consumption (MJ/km) | Cost per unit of energy (€/MJ) | Cost per km (€) | Lifetime fuel consumption cost (200,000 km) (€)
Diesel | 3,9 | 0,039 | 36 | 1,404 | 0,02075 | 0,029136 | 5.827,30
Petrol | 4,7 | 0,047 | 32 | 1,504 | 0,02075 | 0,031211 | 6.242,35
Electric | 17,3 (kWh) | 0,173 | 3,6 | 0,6228 | 0,02075 | 0,012924 | 2.584,93
Hybrid | 3,8 | 0,038 | 32 | 1,216 | 0,02075 | 0,025235 | 5.047,01
CNG | 7,7 (Nm3) | 0,077 | 33 | 2,541 | 0,02075 | 0,052732 | 10.546,42
Ethanol | 7,1 | 0,071 | 21 | 1,491 | 0,02075 | 0,030941 | 6.188,40
Notes: Lets get the most complex part out of the way first…
Fuel consumption known factor, then convert it, use the conversion factor stipulated by the CVD – this can then be converted to MJ/km, the cost per unit of energy is calculated using a reference fuel = the lowest without tax of diesel or petrol, which gives cost per kilometre then times that by the mileage…
You may be asked why CNG is so much more costly – its simply because it is not as energy efficient.
<number>

## Slide 12: OPERATIONAL LIFETIME COSTS – CO2
Vehicle type | CO2 emissions (g/km) | CO2 emissions (kg/km) | Cost (€/kg CO2) | Lifetime CO2 emissions cost (200,000 km) (€)
Diesel | 102 | 0,102 | 0,03 | 612
Petrol | 109 | 0,109 | 0,03 | 654
Electric | 0 | 0 | 0,03 | 0
Hybrid | 87 | 0,087 | 0,03 | 522
CNG | 138 | 0,138 | 0,03 | 828
Ethanol | 116 | 0,116 | 0,03 | 696
.
Notes: [1] The cost allocated in the CVD is 0.03 – 0.04 €/kg CO2, but purchasers may choose to increase to up to 0.08 (i.e. double)
<number>

## Slide 13: OPERATIONAL LIFETIME COSTS - NOX
Vehicle type | NOx emissions (g/km) | Cost (€/g NOx) | Lifetime NOx emissions cost (200,000 km) (€)
Diesel | 0,1225 | 0,0044 | 107,80
Petrol | 0,0416 | 0,0044 | 36,61
Electric | 0 | 0,0044 | 0,00
Hybrid | 0,0033 | 0,0044 | 2,90
CNG | 0,043 | 0,0044 | 37,84
Ethanol | 0,012 | 0,0044 | 10,56
Notes: This shows the relatively higher levels of NOx from diesel, but that a relatively low value is attributed to local air pollution emissions compared to energy efficiency.
Again, the value can be doubled – i.e. Anywhere between 0,0044 – 0,0088.
<number>

## Slide 14: OPERATIONAL LIFETIME COSTS - NMHC
Vehicle type | NMHC emissions (g/km) | Cost (€/g NMHC) | Lifetime NMHC emissions cost (200,000 km) (€)
Diesel | 0 | 0,001 | 0
Petrol | 0,0552 | 0,001 | 11,04
Electric | 0 | 0,001 | 0
Hybrid | 0,0251 | 0,001 | 5,02
CNG | 0 | 0,001 | 0
Ethanol | 0,0564 | 0,001 | 11,28
Notes: This demonstrates the fairly limited weighting (values) given to NMHC emissions
Again, the value can be doubled – i.e. Anywhere between 0,001 – 0,002.
<number>

## Slide 15: OPERATIONAL LIFETIME COSTS - PM
Vehicle type | PM emissions (g/km) | Cost (€/g PM) | Lifetime PM emissions cost (200,000 km) (€)
Diesel | 0,000011 | 0,087 | 0,1914
Petrol | 0,0000168 | 0,087 | 0,29232
Electric | 0 | 0,087 | 0
Hybrid | 0 | 0,087 | 0
CNG | 0 | 0,087 | 0
Ethanol | 0,0000026 | 0,087 | 0,04524
Notes: This demonstrates the limited weighting given to PM
Again, the value can be doubled – i.e. Anywhere between 0,087 – 0,174.
<number>

## Slide 16: OPERATIONAL LIFETIME COSTS - OVERVIEW
Vehicle type | Lifetime costs (€) |  |  |  |  | Total OLC (€)
 | Fuel consumption | CO2 emissions | NOx emissions | NMHC emissions | Particulate emissions | 
Diesel | 5.827,30 | 612 | 107,80 | 0 | 0,191400 | 6.547,29
Petrol | 6.242,35 | 654 | 36,61 | 11,040 | 0,292320 | 6.944,29
Electric | 2.584,93 | 0 | 0 | 0 | 0 | 2.584,93
Hybrid | 5.047,01 | 522 | 2,90 | 5,020 | 0 | 5.576,93
CNG | 10.546,42 | 828 | 37,84 | 0 | 0 | 11.412,26
Ethanol | 6.188,40 | 696 | 10,56 | 11,280 | 0,045240 | 6.906,28
Notes: This is a good overview of the relative weight of each factor of the OLC. Note the dominance of fuel consumption in the final figure.
<number>

## Slide 17: NOTES ON OPTION 3: UNDERSTANDING THE DETAIL
Notes: <number>

## Slide 18: STICKY BITS
    Procurers are dissuaded from using option 3 as part of their procurement exercises due to the following:
        The (perceived) level of complexity
        Some believe it doesn’t value local air pollutants high enough
        Difficulty in getting the relevant information (especially for HDVs)
Notes:       In terms of the values attributed to the emissions, you may want to read and or refer trainees in to the study by PriceWaterHouse (http://ec.europa.eu/transport/themes/urban/studies/doc/2007_ia_dir_clean_efficient_vehicles.pdf) that came up with the values in the first place. You may also want to discuss the problems referred to in Module one, with many cities breaching NOx emission thresholds. In this instance, specifying low emission technology types or technical specifications for local emission levels could be used (i.e. option one under the CVD)
      You may want to mention that some authorities think they are using methodology 3, when in actual fact they are not. This occurs most frequently when they monetise emissions according to the values set out under the CVD, but then convert these into points or weight them in some way – rather than using them as costs which are simply added to the overall LCC calculation.
<number>

## Slide 19: STICKY BITS
Commonly cited issues with the use of methodology 3 include:
    Giving energy consumption a relatively high weighting
    Counting CO2 emissions as well as energy consumption
    Giving a relatively low value to local pollutant emissions
Notes: These are seen by some as being detrimental to the introduction of alternative technologies that are less energy efficient, but have attributes such as zero tail pipe emissions
These issues can be tested when going through methodology 3 more closely in module 4 on life cycle costing
<number>

## Slide 20: STICKY BITS
Commonly cited issues with the use of methodology 3 include:
    Well to wheel (WTW) emissions are not taken into account
        Additional measures must therefore be used as part of the procurement process in order to take into account WTW emissions – however the values and method itself stipulated under the CVD must remain the same
Notes: Other measures could include stipulating low environmental impact production methods for fuels/energy sources used (waste rather than purpose grown crops for biofuels or renewable electricity) as part of the technical specifications.
<number>

## Slide 21: CONCLUSIONS
    Option 3 of the CVD is perceived to be complex but the options under the CVD do offer a great deal of flexibility to procurers
    It requires key environmental factors to be taken into account by procurers, helping to raise the bar & stimulate the clean vehicle market
    Help is at hand! If you have any specific queries on the CVD, other aspects of clean vehicle procurement or require assistance with tendering – do not hesitate to contact the Clean Fleets Helpdesk for free advice!
Notes: Emphasise that all other vehicle related legislation is targeted at manufacturers and therefore it is important to have legislation in place that encourages procurers, especially those who’s commitment to environmental concerns is not necessarily guaranteed.
    The Euro Standards and CO2 limits for manufacturers have been very successful in introducing new, cleaner vehicles onto the market, but these are targeted more at removing the worst performers from the market – the ambition of the CVD is to promote the best performers. In addition,
    The Euro standards and CO2 levels only apply to newly manufactured vehicles whereas many public authorities and/or their public transport operators buy second hand (used) vehicles.
Be aware of the issues associated with the CVD, but consider how you will present them to your audience in order to still encourage them to use the CVD with the spirit of which it was intended.
<number>

## Slide 22: 4.3: THE CLEAN FLEETS LCC TOOL
Notes: This is the Excel tool provided as part of your training materials – reiterate to trainees that values should only be input into the white boxes within the tool, the yellow table to the right hand side of the tool is for use within the formulas only and should not be changed, whereas the small table beneath the tool may be changed as appropriate.
<number>

## Slide 23: THE CLEAN FLEETS LCC TOOL
What is it?

## Slide 24: THE CLEAN FLEETS LCC TOOL
What is it?
    An Excel spreadsheet...
    ...which aims to make life easier for procurers who wish to buy clean, energy efficient vehicles...
    ...by including a series of pre-set formulas...
    ...and the facility to change certain parameters...
    ...used to determine LCC associated with cars & vans..
    ...including operational lifetime costs (OLC) prescribed by the CVD

## Slide 25: THE CLEAN FLEETS LCC TOOL
What does it take into account?
    Acquisition (buying or leasing vehicles or batteries)
    Maintenance (Cost for servicing or Service agreement)
    Taxes and other costs (Tax, insurance & other charges)
    OLC environmental costs (CO2, pollutants, energy use)
    Remnant value
    Infrastructure costs

## Slide 26: THE CLEAN FLEETS LCC TOOL
Questions to bear in mind when testing it
    Would there be any issues with collecting reliable data for the tool?
    Which, if any, aspects are not taken into account correctly?
    Which are not taken into account at all?
    How useful is the Clean Fleets LCC Tool?
    Which improvements could be made?
    .Let’s have a look!
Notes: Activity to carry out with your trainees – in small groups ask them to access the Clean Vehicle Portal on the laptops provided – and using the same size cars, use the lifetime emissions costs provided on the clean vehicle portal to test out the LCC tool. Additional information as to acquisition costs etc. Can be pre-prepared by you and provided to trainees, or if you have time during this slot, ask them to search online for these parameters to input into the tool.
Please do collect any feedback as to improvements that could be made to the tool, as it is still a work in progress!
<number>

## Slide 27: THE CLEAN FLEETS TOOL
    Can be a useful way of calculating life cycle costs including operational lifetime costs (OLC) as one of the options prescribed be the CVD
    Any LCC tool is only as reliable as the data used to complete it
    Feedback is welcomed!